Formulas for Grand Tour:

From Planet1 to Planet3 using 'Swing By' at Planet2

Free movement between Planet1 and Planet2:
All possible ellipses, that touch P1 and P2

r1=1 ; psi1=0 (Position of Planet1)
r2=2 ; psi2=1.76 (Position of Planet2)

phi = atan((r1*sin(psi1)-r2*sin(psi2))/(r1*cos(psi1)-r2*cos(psi2)))
exc = 2*r1*cos(psi1+phi)

Choose any kk (Rotation of ellipses itself)

#excentricity of ellipse
  exc = (r2 - r1) / (r2*cos(psi2-kk) – r1*cos(psi1-kk))
#main axis of ellipses
  ha = r2 * (1 - exc * cos(psi2 - kk)) / (1 - exc*exc)

#Polar function of ellipse
#rad = ha*(1-exc*exc)/(1-exc*cos(zz-kk))

#velocity when reaching near of Planet2
v2 = massSun*G*(2/r2 – 1/ha)

#Angle when reaching near of Planet2
alpha2 = arccos((1+exc*cos(psi2))/sqrt(1+2*exc*cos(psi2)+exc*exc))
#or
alpha2 = arcsin(exc*sin(psi2)/sqrt(1+2*exc*cos(psi2)+exc*exc))

# FlyBy at Planet p (hier 2)
# Variate distanceFromGround
#(may later extend to variate additional accelaration)

# Input is end of free flight
Vin=v2 ; alphaIn=alpha2
#dist = radiusPlanet + distanceFromGround

# Velocity relative to planet:
Vu = sqrt(Vu*Vu+Vp*Vp-2*Vu*Vp*cos(alphaIn))

#Parameters of FlyBy Hyperbel
exc = 1 + (dist*Vu*Vu/(massPlanet*G))
#h = omegaS*rS*rS
#h = dist*sqrt(Vu*Vu+(2*massPlanet*G/dist))

#Normalized distance
distance=dist*sqrt((exc+1)/(exc-1))
distanceP = Vp*Vp*delta/(massPlanet*G)
#check: distance>sqrt(Sqr(radiusPlanet+massPlanet*G/(Vu*Vu)) - Sqr(massPlanet*G/(Vu*Vu)))

#Change of flight angle
delta = 2*arctan(Vp*Vp/(distanceP*Vu*Vu))
#or
delta = 2*arcsin(1/exc)

#Velocity after FlyBy (relative to sun)
Vout=Vin+Vin*2/(sqrt(1+Sqr(delta*Vin*Vin/(massPlanet*G))))

#Angle after FlyBy (relative to sun)
alphaOut=alphaIn+delta

#Calculate new ellipse parameters